Open Headset Interconnect Standard
Mark Smith, N6MTS

---
Who am I?
Mark Smith, N6MTS
Head Cheese, Halibut Electronics: https://electronics.halibut.com/
A host of the Ham Radio Workbench Podcast:
https://www.hamradioworkbench.com/
Twitter and YouTube: @SmittyHalibut
Mastodon/Fediverse: @smitty@halibut.com
Video

---
Who am I?
Ham: Active ham since 1992.
College: Two years in Electrical Engineering, but degree in Computer Engineering
Work: 25 years in IT, Network and Unix Systems Engineering, and Information Security.
All Three: Left IT in 2021, started Halibut Electronics to make Ham Radio and Audiophile electronics.
First big product, SOAR: Satellite Optimized Amateur Radio. Available late 2022.

---
Open Headset Interconnect Standard
Open: Any individual or company may make devices compliant with this standard, with no obligation.
Headset: Describes the signaling commonly found between a user and a radio: Microphone, Headphones, and Push To Talk.
Interconnect: Describes both the physical and electrical connection of those signals between the user and radio.
Standard: Devices built to this standard will work with other devices built to the same standard.

---
Standards
We have electrical standards (defined, or defacto) for things like RF and Power:
RF: 50 ohm impedance coax, 450 ohm twin lead
Power: +13.8vDC +/- 15%

---
Standards
And one, or a few, physical standards that are easy to convert between:
RF: PL-259, Type N, BNC, etc
Power: Powerpole, 6-pin “Molex”, “T” blades, etc

---
Standards?
No such electrical standards exist for the User to Radio interface:
Microphone: Dynamic, Electret, or Carbon? Balanced or single ended?
Audio out: Headphone level, speaker level, or line level? Ground referenced or push-pull? Mono or stereo?
PTT: GPIO style contact closure to ground, or completing the mic circuit?

---
So many to choose from!
There are even more physical options to choose from!
Microphone: 3.5mm TS/TRS? ¼” TS/TRS? XLR? “8-pin round” Aviation? 8 pin modular? 6 pin modular? What pinout?
Audio out: 3.5mm TS/TRS? ¼” TS/TRS?
PTT: On the mic connector? 3.5mm TS? ¼” TS?

---
The problem is...
Yaesu FT-920 Microphone pinout:
Heil Pro 7 Headset:

---
The solution?
Heil AD-1-Y Adapter:
Yaesu FT-920 Microphone pinout:
Yaesu FT-920 Microphone pinout:
Heil Pro 7 Headset:

---
But, I’ve got a Kenwood too.
Yaesu FT-920 Microphone pinout:
Yaesu FT-920 Microphone pinout:
Kenwood TS-890S Microphone pinout:
Kenwood TS-890S Microphone pinout:

---
But, I’ve got a Kenwood too.
Heil Pro 7 Headset:
Kenwood TS-890S Microphone pinout:

---
Bob has me covered...
Heil AD-1-K Adapter:
Heil Pro 7 Headset:
Kenwood TS-890S Microphone pinout:

---
What about Icom?
Icom IC-7300 Microphone pinout:
Heil Pro 7 Headset:

---
Same connect-- oh… Never mind...
Yaesu FT-920 Microphone pinout:
Icom IC-7300 Microphone pinout:
Kenwood TS-890S Microphone pinout:

---
What about Icom?
Icom IC-7300 Microphone pinout:
Heil Pro 7 Headset:

---
Bob still has me covered...
Heil AD-1-iC Adapter:
Icom IC-7300 Microphone pinout:
Heil Pro 7 Headset:

---
But, wait a minute...
Heil AD-1-iC Adapter:
Icom IC-7300 Microphone pinout:
Heil Pro 7 Headset:
Heil P7-IC-ELEM Microphone Element:

---
Another headset,
CTIA “PC Gaming Headset”
or “Mobile Phone” pinout:
Yaesu FT-920 Microphone pinout:

---
Another headset, 3 more adapters...
CTIA “PC Gaming Headset”
or “Mobile Phone” pinout:
Yaesu FT-920 Microphone pinout:
Kenwood TS-890S Microphone pinout:
Icom IC-7300 Microphone pinout:

---
“Your audio is distorted!”
CTIA “PC Gaming Headset”
or “Mobile Phone” pinout:
Yaesu FT-920 Microphone pinout:

---
Which 3.5mm TRRS was that?
CTIA “PC Gaming Headset”
or “Mobile Phone” pinout:

---
Which 3.5mm TRRS was that?
CTIA “PC Gaming Headset”
or “Mobile Phone” pinout:

---
Your Adapter Game is strong.
This is quickly getting out of hand.
It’s a full mesh of adapters, from every different headset to every different radio.
How do we address this?

---
Open Headset Interconnect Standard
User side adapter: Specific to the headset, stays with the headset.
Radio side adapter: Specific to the radio, stays with the radio.
Open Headset Interconnect Standard is the connection between them.

---
Technical Summary
Physical:
Connector: 8P8C Modular. (Commonly, but incorrectly, known as RJ-45.)
Cable: Cat5 or better. Shielded is preferred but not required.
Wiring: TIA-568A or 568B. Which pins pairs are on is important.
Allows the use of common off-the-shelf Ethernet cables.

---
Technical Summary
Electrical:
Microphone: Electret level. +5vDC bias provided by Radio.
Audio Out: Ground referenced, “Headphone” level, stereo.
PTT: Simple contact closure to ground.
Power: +5vDC 200mA provided by Radio for audio amplifiers, LED indicators, signal processing, etc.

---
Technical Summary
Pin-out:

---
Technical Summary
Pin-out:

---
Dynamic Mic Preamp

---
Technical Details...
See the Groups.io email list and GitHub repository at the end of this presentation.

---
When is OHIS useful?
When you have several different radios and headsets.
When you operate in a shared environment and different users have their own headsets.
Examples: Field Day, club shack, or an Emergency Operations Center
When you want to design and sell a device that goes between the User and the Radio, and have it work everywhere without overly complex input and output interfacing.
ahem

---
When is OHIS over-kill?
When you only have one radio, or one headset, or any situation where the “full mesh” problem doesn’t apply.
When you already have all the adapters you need.
When you prefer the simplicity of a single adapter between you and your radio.

---
Why an Open Standard?
Halibut Electronics needed to solve this problem for future products.
I am not Gillette.
This is a good DIY project, and I love DIY projects.
Obviously, Halibut Electronics will sell adapters for people who don’t want to have to solve it themselves. But I hope other companies will adopt the standard and sell adapters too.

---
Learn more
Groups.io mailing list:
https://halibut-electronics.groups.io/open-headset-interconnect-standard/
GitHub repository:
https://github.com/Halibut-Electronics/Open-Headset-Interconnect-Standard

---
Questions and Answers
Beginning now

---
Slide Title
Slide Content