## Slide 1
Open Headset Interconnect Standard
Mark Smith, N6MTS
https://ohis.org/

## Slide 2
Video
Who am I?
Mark Smith, N6MTS
President/CEO, Halibut Electronics: https://electronics.halibut.com/
A host of the Ham Radio Workbench Podcast: https://www.hamradioworkbench.com/
YouTube: @SmittyHalibut
Mastodon/Fediverse: @smitty@halibut.com
https://ohis.org/

## Slide 3
Video
Who am I?
Mark Smith, N6MTS
President/CEO, Halibut Electronics: https://electronics.halibut.com/
A host of the Ham Radio Workbench Podcast: https://www.hamradioworkbench.com/
YouTube: @SmittyHalibut
Mastodon/Fediverse: @smitty@halibut.com
https://ohis.org/
Head Cheese

## Slide 4
Video
Who am I?
Ham: Active ham since 1992.
College: Two years in Electrical Engineering, but degree in Computer Engineering, CalPoly San Luis Obispo
Work: ~30 years in IT, Network and Unix Systems Engineering, and Information Security.
All Three: Left IT in 2021, started Halibut Electronics to make Ham Radio and Audiophile electronics.
https://ohis.org/

## Slide 5
Video
Open Headset Interconnect Standard
https://ohis.org/

## Slide 6
Video
Open Headset Interconnect Standard
https://ohis.org/
Open: Any individual or company may make devices compliant with this standard, with no obligation.

## Slide 7
Video
Open Headset Interconnect Standard
https://ohis.org/
Open: Any individual or company may make devices compliant with this standard, with no obligation.
Headset: Describes the signaling commonly found between a user and a radio: Microphone, Headphones, and Push To Talk.

## Slide 8
Video
Open Headset Interconnect Standard
https://ohis.org/
Open: Any individual or company may make devices compliant with this standard, with no obligation.
Headset: Describes the signaling commonly found between a user and a radio: Microphone, Headphones, and Push To Talk.
Interconnect: Describes both the physical and electrical connection of those signals between the user and radio.

## Slide 9
Video
Open Headset Interconnect Standard
https://ohis.org/
Open: Any individual or company may make devices compliant with this standard, with no obligation.
Headset: Describes the signaling commonly found between a user and a radio: Microphone, Headphones, and Push To Talk.
Interconnect: Describes both the physical and electrical connection of those signals between the user and radio.
Standard: Devices built to this standard will work with other devices built to the same standard.

## Slide 10
Video
Electrical Standards
https://ohis.org/
We have electrical standards (defined, or de-facto) for things like RF and Power:

## Slide 11
Video
Electrical Standards
https://ohis.org/
We have electrical standards (defined, or de-facto) for things like RF and Power:
RF: 50 ohm impedance coax, 450 ohm twin lead

## Slide 12
Video
Electrical Standards
https://ohis.org/
We have electrical standards (defined, or de-facto) for things like RF and Power:
RF: 50 ohm impedance coax, 450 ohm twin lead
Power: +13.8vDC +/- 15%

## Slide 13
Video
Physical Standards
https://ohis.org/
And one, or a few, physical standards that are easy to convert between:

## Slide 14
Video
Physical Standards
https://ohis.org/
And one, or a few, physical standards that are easy to convert between:
RF: PL-259, Type N, BNC, etc

## Slide 15
Video
Physical Standards
https://ohis.org/
And one, or a few, physical standards that are easy to convert between:
RF: PL-259, Type N, BNC, etc
Power: Powerpole, 6-pin “Molex”, “T” blades, etc

## Slide 16
Video
Headset Standards?
https://ohis.org/
No such electrical standards exist for the User to Radio interface:

## Slide 17
Video
Headset Standards?
https://ohis.org/
No such electrical standards exist for the User to Radio interface:
Microphone: Dynamic, Electret, or Carbon? Balanced or single ended?

## Slide 18
Video
Headset Standards?
https://ohis.org/
No such electrical standards exist for the User to Radio interface:
Microphone: Dynamic, Electret, or Carbon? Balanced or single ended?
Audio out: Line level, headphone level, or speaker level? Ground referenced or push-pull? Mono or stereo?

## Slide 19
Video
Headset Standards?
https://ohis.org/
No such electrical standards exist for the User to Radio interface:
Microphone: Dynamic, Electret, or Carbon? Balanced or single ended?
Audio out: Line level, headphone level, or speaker level? Ground referenced or push-pull? Mono or stereo?
PTT: GPIO style contact closure to ground, or completing the mic circuit?

## Slide 20
Video
So many to choose from!
https://ohis.org/
There are even more physical options to choose from!

## Slide 21
Video
So many to choose from!
https://ohis.org/
There are even more physical options to choose from!
Microphone: 3.5mm TS? TRS? XLR? “8-pin round?” RJ-45? What’s the pinout?

## Slide 22
Video
So many to choose from!
https://ohis.org/
There are even more physical options to choose from!
Microphone: 3.5mm TS? TRS? XLR? “8-pin round?” RJ-45? What’s the pinout?
Audio out: 3.5mm TS? TRS? ¼ inch TS? TRS? RCA?

## Slide 23
Video
So many to choose from!
https://ohis.org/
There are even more physical options to choose from!
Microphone: 3.5mm TS? TRS? XLR? “8-pin round?” RJ-45? What’s the pinout?
Audio out: 3.5mm TS? TRS? ¼ inch TS? TRS? RCA?
PTT: On the mic connector? Separate 3.5mm TS? ¼ inch Footswitch?

## Slide 24
Video
The problem is...
Heil Pro 7 Headset:
Yaesu FT-920 Microphone pinout:
https://ohis.org/

## Slide 25
Video
The solution?
Heil AD-1-Y Adapter:
Yaesu FT-920 Microphone pinout:
Heil Pro 7 Headset:
https://ohis.org/

## Slide 26
Video
But, I’ve got a Kenwood too.
Kenwood TS-890S Microphone pinout:
Yaesu FT-920 Microphone pinout:
https://ohis.org/

## Slide 27
Video
But, I’ve got a Kenwood too.
Kenwood TS-890S Microphone pinout:
Heil Pro 7 Headset:
https://ohis.org/

## Slide 28
Video
Bob has me covered...
Heil Pro 7 Headset:
Kenwood TS-890S Microphone pinout:
Heil AD-1-K Adapter:
https://ohis.org/

## Slide 29
Video
What about Icom?
Heil Pro 7 Headset:
Icom IC-7300 Microphone pinout:
https://ohis.org/

## Slide 30
Video
Same connect-- oh… Never mind...
Icom IC-7300 Microphone pinout:
Yaesu FT-920 Microphone pinout:
Kenwood TS-890S Microphone pinout:
https://ohis.org/

## Slide 31
Video
What about Icom?
Heil Pro 7 Headset:
Icom IC-7300 Microphone pinout:
https://ohis.org/

## Slide 32
Video
Bob still has me covered...
Heil Pro 7 Headset:
Icom IC-7300 Microphone pinout:
Heil AD-1-iC Adapter:
https://ohis.org/

## Slide 33
Video
But, wait a minute...
Heil Pro 7 Headset:
Icom IC-7300 Microphone pinout:
Heil AD-1-iC Adapter:
Heil P7-IC-ELEM Microphone Element:
https://ohis.org/

## Slide 34
Video
Another headset,
Yaesu FT-920 Microphone pinout:
CTIA “PC Gaming Headset” or “Mobile Phone” pinout:
https://ohis.org/

## Slide 35
Video
Another headset, 3 more adapters...
Yaesu FT-920 Microphone pinout:
CTIA “PC Gaming Headset” or “Mobile Phone” pinout:
Kenwood TS-890S Microphone pinout:
Icom IC-7300 Microphone pinout:
https://ohis.org/

## Slide 36
Video
“Your audio is distorted!”
Yaesu FT-920 Microphone pinout:
CTIA “PC Gaming Headset” or “Mobile Phone” pinout:
https://ohis.org/

## Slide 37
Video
Your Adapter Game is strong.
https://ohis.org/
This is quickly getting out of hand.
It’s a full mesh of adapters, from every different headset to every different radio.

## Slide 38
Video
Your Adapter Game is strong.
https://ohis.org/
This is quickly getting out of hand.
It’s a full mesh of adapters, from every different headset to every different radio.
How do we address this?

## Slide 39
Video
Your Adapter Game is strong.
This is quickly getting out of hand.
It’s a full mesh of adapters, from every different headset to every different radio.
How do we address this?
https://ohis.org/

## Slide 40
Video
Open Headset Interconnect Standard
https://ohis.org/

## Slide 41
Video
Open Headset Interconnect Standard
https://ohis.org/
User Device/Adapter: Specific to the headset, stays with the headset.

## Slide 42
Video
Open Headset Interconnect Standard
https://ohis.org/
User Device/Adapter: Specific to the headset, stays with the headset.
Radio Device/Adapter: Specific to the radio, stays with the radio.

## Slide 43
Video
Open Headset Interconnect Standard
https://ohis.org/
User Device/Adapter: Specific to the headset, stays with the headset.
Radio Device/Adapter: Specific to the radio, stays with the radio.
Open Headset Interconnect Standard is the connection between them.

## Slide 44
Video
Technical Summary
https://ohis.org/
Electrical:

## Slide 45
Video
Technical Summary
https://ohis.org/
Electrical:
Microphone: “Electret” level: -45dBV +/- 3dB, pseudo-balanced. +5vDC bias provided by Radio Device.

## Slide 46
Video
Technical Summary
https://ohis.org/
Electrical:
Microphone: “Electret” level: -45dBV +/- 3dB, pseudo-balanced. +5vDC bias provided by Radio Device.
Audio Out: “Headphone” level: 0dBV full volume, ground referenced, stereo.

## Slide 47
Video
Technical Summary
https://ohis.org/
Electrical:
Microphone: “Electret” level: -45dBV +/- 3dB, pseudo-balanced. +5vDC bias provided by Radio Device.
Audio Out: “Headphone” level: 0dBV full volume, ground referenced, stereo.
PTT: Contact closure to power ground.

## Slide 48
Video
Technical Summary
https://ohis.org/
Electrical:
Microphone: “Electret” level: -45dBV +/- 3dB, pseudo-balanced. +5vDC bias provided by Radio Device.
Audio Out: “Headphone” level: 0dBV full volume, ground referenced, stereo.
PTT: Contact closure to power ground.
Power: (Optional) +5vDC 200mA provided by Radio for audio amplifiers, LED indicators, signal processing, etc.

## Slide 49
Video
Technical Summary
https://ohis.org/
Physical:

## Slide 50
Video
Technical Summary
https://ohis.org/
Physical:
Connector: 8P8C Modular. (Commonly, but incorrectly, known as RJ-45.)

## Slide 51
Video
Technical Summary
https://ohis.org/
Physical:
Connector: 8P8C Modular. (Commonly, but incorrectly, known as RJ-45.)
Cable: Shielded Cat5 (or better).

## Slide 52
Video
Technical Summary
https://ohis.org/
Physical:
Connector: 8P8C Modular. (Commonly, but incorrectly, known as RJ-45.)
Cable: Shielded Cat5 (or better).
Wiring: TIA-568A or 568B. Which pins are pairs is important.

## Slide 53
Video
Technical Summary
https://ohis.org/
Physical:
Connector: 8P8C Modular. (Commonly, but incorrectly, known as RJ-45.)
Cable: Shielded Cat5 (or better).
Wiring: TIA-568A or 568B. Which pins are pairs is important.
Allows the use of common off-the-shelf Ethernet cables.

## Slide 54
Video
Technical Summary
Pin-out:
https://ohis.org/

## Slide 55
Video
Technical Summary
Pin-out:
https://ohis.org/

## Slide 56
Video
Dynamic Mic Pre-Amp
Part of the open standard, freely available for use.
https://ohis.org/

## Slide 57
Video
When is OHIS useful?
https://ohis.org/

## Slide 58
Video
When is OHIS useful?
When you have several different radios and headsets.
https://ohis.org/

## Slide 59
Video
When is OHIS useful?
When you have several different radios and headsets.
When you operate in a multi-user environment and users have their own (different) headsets.
https://ohis.org/

## Slide 60
Video
When is OHIS useful?
When you have several different radios and headsets.
When you operate in a multi-user environment and users have their own (different) headsets.
  Examples: Field Day, club shack, or an Emergency Operations Center.
https://ohis.org/

## Slide 61
Video
When is OHIS useful?
When you have several different radios and headsets.
When you operate in a multi-user environment and users have their own (different) headsets.
  Examples: Field Day, club shack, or an Emergency Operations Center.
To present a common electrical interface for devices between the user and the radio.
https://ohis.org/

## Slide 62
Video
When is OHIS over-kill?
https://ohis.org/

## Slide 63
Video
When is OHIS over-kill?
When you only have one radio, or one headset, or any situation where the “full mesh” problem doesn’t apply.
https://ohis.org/

## Slide 64
Video
When is OHIS over-kill?
When you only have one radio, or one headset, or any situation where the “full mesh” problem doesn’t apply.
When you already have all the adapters you need.
https://ohis.org/

## Slide 65
Video
When is OHIS over-kill?
When you only have one radio, or one headset, or any situation where the “full mesh” problem doesn’t apply.
When you already have all the adapters you need.
When you prefer the simplicity of a single adapter between you and your radio.
https://ohis.org/

## Slide 66
Video
Why an Open Standard?
https://ohis.org/

## Slide 67
Video
Why an Open Standard?
Open is how we get out of this mess.
https://ohis.org/

## Slide 68
Video
Why an Open Standard?
Open is how we get out of this mess.
It makes a good DIY project.
https://ohis.org/

## Slide 69
Video
Learn more:
https://ohis.org/
https://ohis.org/

## Slide 70
Questions and Answers
Beginning now

## Slide 71
Video
Slide Title
Slide Content